## Slide 1: An Integrated High-throughput Workflow for Identification of Crosslinked Peptides
Bing Yang
National Institute of Biological Sciences, Beijing
Yan-Jie Wu
Institute of Computing Technology,
Chinese Academy of Sciences CNCP 2012, Beijing

## Slide 2: CXMS: Chemical Crosslinking coupled with Mass Spectrometry

## Slide 3: Advantages of CXMS
Identify direct binding proteins
beads
antibody
bait
P1
P2
P3
P1, P2, P3 can co-IP with the bait by either direct or indirect interaction
Crosslinking of P1 and the bait, if detected, suggests direct binding

## Slide 4: Advantages of CXMS
Identify direct binding proteins
Study protein folding

## Slide 5: Advantages of CXMS
Identify direct binding proteins
Study protein folding
Analyze protein complex assembly

## Slide 6: Major Challenges
Crosslinked samples are extremely complex
Regular
Mono-linked (Type 0)
Loop-linked (Type 1)
Inter-linked (Type2)
Normal sample
Crosslinked sample
Regular

## Slide 7: Major Challenges
116KD
66.2KD
45KD
35KD
Cyclin T1
CDK9
CDK9/Cyclin T1
many a few a few
Trypsin digestion
Low abundance of Inter-linked peptides

## Slide 8: Major Challenges
Highly complex MS2 spectra
Regular peptides
Crosslinked peptides

## Slide 9: Major Challenges
Database can be huge
If the routine search space is 100 peptides,
the crosslink search space is 5,050 pairs.
Database | Proteins | Peptides | Peptide Pairs
E. coli | 6126 | 3.35*105 | 5.63*1010(104 times the human db)
C. elegans | 24652 | 1.18*106 | 6.96*1011

## Slide 10: Major Challenges
Crosslinked samples are extremely complex
Low abundance of Inter-linked peptides
Highly complex MS2 spectra
Database can be huge
Difficult to estimate false discovery rates
Limited software

## Slide 11: Overcome the Challenges in CXMS
Crosslinked samples are extremely complex
Low abundance of Inter-linked peptides
Select only ≥ +3 charged precursors for MS2

## Slide 12: Overcome the Challenges in CXMS
Highly complex MS2 spectra
Huge database
Difficult to estimate false discovery rates
Limited software
Collaborating with the pFind group of ICT, we developed pLink specifically for CXMS data analysis.

## Slide 13: pLabel is Developed to Annotate Crosslink Spectra

## Slide 14: Generating a Standard Dataset for the pLink Software
Synthesized 38 peptides, X…X-K-X…X(K/R), each 5-28 aa long
Crosslinked all possible peptide pairs–741 in total–with an amine specific crosslinker BS3
Light BS3 d0
Heavy BS3 d4

## Slide 15: Isotope-coding Helps Recognize Peptides Carrying the Cross-linker
H
H
H
H
D
D
D
D
Light Linker (L)
Heavy Linker (H)
Proteins
Crosslink with L/H (1:1)
Digestion and LC-MS
Xlinked peptides
L/H Intensity ratio 1:1

## Slide 16: Generating a Standard Dataset for the pLink Software
Synthesized 38 peptides, X…X-K-X…X(K/R), each 5-28 aa long
Crosslinked all possible peptide pairs–741 in total–with an amine specific crosslinker BS3
Each reaction was analyzed in a 35-min reverse phase LC-MS/MS experiment.
2077 pairs of crosslinked peptides, including isoforms, were identified from HCD spectra.

## Slide 17: Each Peptide Pair can be Crosslinked into Different Isoforms

## Slide 18: Most Prominent Ions in the HCD Spectra of Crosslinked Peptides
From 2077 Spectra, in descending order of prominence:
y1+
y2+
b1+
yb1+ (including by, yb, by, by)
b2+
ya1+ (including ay, ya, ay, ay)
a1+
y3+
αL/βL (α or β with a cleaved linker attached)
b3+
a2+
KLα/KLβ (α or β linked to the immonium ion of K)

## Slide 19
Ion types specific for crosslinked peptides
yb1+ (including by, yb, by, by)
ya1+ (including ay, ya, ay, ay)
αL/βL (α or β with a cleaved linker
KLα/KLβ (α or β linked to the immonium ion of K)
Most Prominent Ions in the HCD Spectra of Crosslinked Peptides

## Slide 20: Examples of yb Ions
b3y2
b3y2

## Slide 21: L or L Ions
L3
L2

## Slide 22: KL/: K-linked  or  Ions
a2y2 /KL

## Slide 23: Considering New Ion Types Improved Scoring
Experiment | Theoretical ion types
Basic | b1+,b2+,y1+,y2+,a1+,a2+
All | b1+, b2+, y1+,y2+, a1+,a2+, yb1+, ya1+, KLα(KLβ),αL(βL) 1+ and αL(βL) 2+
In pLink, the scoring function for spectrum-peptide matching is based on the Kernel Spectral Dot Product (KSDP) algorithm developed by Fu et al. in 2004 (the pFind search engine).
–Log10 (E-value)
#of spectra

## Slide 24: The Open-search Mode for Large Databases
Open Database Search
PreScore against peptides w/ mass < precursor
Treat mass as modification on K
K
K
K
K
K
K
…
Pep mass (w/o modification)  or  0.5*precursor?
α peptides
β peptides
K
K
K
…
K
K
K
…


Pair up top 500 α and β peptides: α + β + linker = precursor
Fine scoring against the candidate pairs

## Slide 25: False Discovery Estimation Based on a Modified Reverse Database Strategy
F
R
+
F-F
R-R
F-R
R-F
Crosslink in silico
T
U
F
Randomly matched spectra fall into T, U, and F at a 1:2:1 ratio
25.0 %
No correct seq in DB
Correct seq added & matches to T increased

## Slide 26: False Discovery Estimation Based on a Modified Reverse Database Strategy
F
R
+
F-F
R-R
F-R
R-F
Crosslink in silico
T
U
F
Among the spectra that match to peptide pairs in T, there are two types of false matches:
Both peptide sequences are wrong
this is estimated by # spectra that match to F (NF), while twice as many (2*NF ) are expected to match to U.
• One peptide correct, the other not
estimated by (Nu – 2*NF )
• So, the total # of false matches = NF + (Nu – 2*NF ) = Nu – NF FDR = (Nu – NF)/NT
1 : 2 : 1

## Slide 27
Performance of pLink
at 5% FDR, large dataset + large database
sensitivity >90%
accuracy >95%
specificity >95%

## Slide 28: CXMS Analysis of GST

## Slide 29: CXMS Result Verified by Crystal Structure
5 out 6 crosslinks are structurally sound (yellow dashed lines)

## Slide 30: CXMS Helped Confirm the Structure of the CNGP Complex
10 out 12 crosslinks consistent with the structure (yellow lines)

## Slide 31: CXMS on a Large Protein Complex of Unknown Structure
UTP-B is a 550 kDa, six-subunit complex involved in ribosome biogenesis, but its structure is unknown.
71 different crosslinked peptide pairs (1337 spectral copies) identified from the purified UTP-B complex
21 between subunits

## Slide 32: CXMS Revealed Subunit Interactions within the UTP-B Complex

## Slide 33: IP with CXMS Identified Direct Binding Proteins of FIB-1
GFP IP + Crosslink
Trypsin Digestion
Mass Spec
NTD
CTD
ce_Nop56
NTD
CTD
CD
ce_Nop58
FIB-1
beads
GFP
MTase
ce_Snu13
CD

## Slide 34: CXMS Results Fit Nicely with a Structural Model of the C. elegans FIB-1 Complex

## Slide 35: 394 Interlinked Peptides were Identified from Crosslinker-treated E. coli Lysate
Chart: 
| intra-molecular | inter-molecular
 | 270 | 124
Inter-molecular
124 (31.5%)
Intra-molecular
270 (68.5%)
Chart: 
| compatible | incompatible | Structure unavailable
 | 179 | 58 | 157
Compatible w/ Structure
179 (75.5%)
Incompatible
58 (24.5%)
Structure unavailable
157
3
4
5
6
7
8
1
2
positive control
negative control
AD-AAA97042.1 + BD-NP_416801.2 (#91)
AD-AAC73200.1 + BD-AAC75219.1 (#98)
AD-NP_416518.2 + BD-AAC73708.1 (#115)
AD-YP_026243.1 + BD-AAA58136.1 (#71)
AD-YP_025307.1 + BD-AAA58136.1 (#69)
AD-AAC74522.1 + BD-AAA58136.1 (#70)
– LW
– LWH
5 out of 8 randomly selected inter-molecular crosslinks verified by Y2H

## Slide 36: Summary
An integrated workflow to identify crosslinked peptides from a wide range of samples.
Does not require isotope-labeling in crosslinker
Works for K-K, K-C, and K-D/E crosslinks
Ready to use for protein-protein interaction and structural analyses

## Slide 37: Acknowledgment
Meng-Qiu Dong (NIBS)
Ming Zhu
Yue-He Ding
Si-Min He (ICT)
Sheng-Bo Fan
Yan-Jie Wu
Kun Zhang
Li-Yun Xiu
Ke-Qiong Ye (NIBS)
Jing-Zhong Lin
Shu-Ku Luo
Shuang Li
She Chen (NIBS)
Andreas Huhmer (Thermo)
Zhiqi Hao
David Horn